7. Heat Treatment of Wood Packaging Material using Dialectric Heat (2007-114)

| Comment no. | Paragraph no. | Comment type | Comment | Explanation | Author |
| --- | --- | --- | --- | --- | --- |
| [1] | 7 | Technical | This treatment applies to the heat treatment of wood packaging material using dielectric heat to reduce the risk of introduction and spread of all pests of wood including Asian longhorned beetle (Anoplophora glabripennis) (ALB), pinewood nematode (Bursaphelenchus xylophilus) (PWN)1 and those pests required to meet the criteria for treatment as prescribed in ISPM 15. | Of all pests, ALB and PNW are the most tolerant to heat treatment. | IPPC Regional Workshop Asia |
| [2] | 13 | Technical | Target regulated articles Debarked wood not exceeding 20 cm in cross-section | The specifiaction on the size of the wood (not exceeding 20cm in cross section) needs to be clarified with the TPPT. | IPPC Regional Workshop Asia |
| [3] | 15 | Technical | Where the application of heat treatment is undertaken using dielectric radiation (e.g. microwaves), wood packaging material composed of wood not exceeding 20 cm in cross-section when measured across the smallest dimension of the piece must be heated to achieve a minimum of 60 ˚C for 1 minute throughout the profile of the wood. Heating to the prescribed temperature must occur within 30 minutes from ambient temperature. | The specifiaction on the size of the wood (not exceeding 20cm in cross section) needs to be clarified with the TPPT. | IPPC Regional Workshop Asia |
| [4] | 17 | Substantive | The dielectric heat treatment provider must be approved by the NPPO. When approving and auditing a heat treatment provider, the National Plant Protection Organization (NPPO) shall ensure that the following factors are appropriately addressed by those involved in treatment: | Clarification | IPPC Regional Workshop Asia |
| [5] | 18 | Substantive | The treatment needs to be monitored where the temperature is likely to be the coldest to ensure the target temperature is maintained. Irrespective of whether the dielectric heat treatment is conducted as a batch process or as a continuous (conveyor) process, if the operator is measuring the surface temperature to estimate compliance with the prescribed standard, the operator should have initially validated through testing that the internal wood temperatures meet or exceed 60 ˚C for 1 minute through the profile of the wood. For measuring the surface temperature at least two temperature sensors should be used. For wood exceeding 5 cm in thickness, dielectric heating at 2.45 GHz may require bidirectional application or multiple waveguides for the delivery of microwave energy to ensure uniformity of heating. For wood less than 5 cm in thickness, uniformity of heating for the chamber should be tested and equipment modified as needed to ensure uniform heating. Temperature sensors including the measurement and recording equipment are calibrated at a frequency specified by the NPPO or its accredited agency. | There are instances that the NPPO is not the agency conducting calibration. | IPPC Regional Workshop Asia |
| [6] | 19 | Technical | Other relevant information | Additional information on the treatment process, appropriate equipment for measurement, monitoring methods, considerations on wood moisture content, etc. should be requested to the TPPT and should be included in this annex. | IPPC Regional Workshop Asia |
| [7] | 20 | Technical | The coldest part of the wood will differ depending on the energy sources or processes applied. When using microwaves as a heating source, the coldest part of the wood is generally the surface. | Effect of microwave depends on the water content of the wood. | IPPC Regional Workshop Asia |